## Slide 1
NISAR Cryosphere ATBD
Cryosphere Lead: Ian Joughin
Science Team: Rick Forster, Alex Gardner, Sean Helfrich, Ben Holt, Eric Rignot, and Bernd Scheuchl

## Slide 2
Overview
Glacier and Ice Sheets:
Requirements
Algorithms
Implementations
Validation/Notebooks
Sea Ice
Requirements
Algorithms
Implementations
Validation/Notebooks

## Slide 3
L2 Requirement 667: Annual ice sheet (> 90% coverage) horizontal velocity with accuracy better than 3% plus 1 m/yr (1-sigma), at 100-m resolution in slow areas (< 50 m/yr).
L2 Requirement 668: Annual ice sheet horizontal velocity (>90% coverage) to an accuracy better than 3% plus 5 m/yr (1-sigma), at 250-m resolution in fast areas (>50 m/yr).
Annual Glacier & Ice Sheet Requirements
Data from MEaSUREs GrIMP

## Slide 4
Glacier & Ice Sheet Time Series Requirement
L2 Requirement 738: Time-varying horizontal velocities at near-weekly sampling intervals in areas of potential rapid or seasonal change to an accuracy better than 3% plus 10 m/yr (1-sigma) at 500-m resolution (> 80% coverage).
Data from MEaSUREs ITS_LIVE

## Slide 5
L2 Requirement 445: The NISAR project shall measure the vertical differential displacement of all floating ice shelves and ice tongues with vertical accuracy of 100 mm at 100-m resolution annually (> 95% coverage) and monthly (>50% coverage).
Grounding Line Requirement
Data from MEaSUREs Antarctica (Rignot et al., 2014)

## Slide 6
ATBD Scope
The project is required to produce L0-L2 products.
The project/ST is not required to produce L3-L4 products for purposes other than cal/val. (Higher level products for some disciplines produced through additional funding, e.g., soil moisture.)
The science team’s role is to generate a sufficient number of products using the algorithms described in the ATBD to demonstrate that the requirements CAN be met.
Cal/val efforts are open science activities so all L3/L4 cal/val products and data will be freely distributed. Possible exception for non-project funded field data contributed by external groups.

## Slide 7
Relevant L0-L2 Products
Speckle-tracked offsets from cross correlation of SLC pairs with error estimates:
Pros:
  Data from two directions (line of sight & azimuth).
  Works well for fast-moving ice.
Cons:
  Coarser resolution (few hundred meters).
  Poorer precision (~1/20 of a several meter pixel).
  Larger ionospheric errors in azimuth direction, especially at L-band.
Unwrapped interferometric phase with error estimates:
Pros:
  High precision (fraction of 24-cm wavelength).
  Fine-resolutions (10s of meters).
  Ionospheric correction.
Cons:
  Difficult/impossible to unwrap for fast moving areas.
  Only line of sight information so at least a second look direction is needed.

## Slide 8
Offsets: For range-azimuth coordinates, , in the reference SLC, cross correlation is used to locate same point, in the second SLC, which is in non-integer values. The raw range and azimuth offsets, , are given by:
.
Phase: For co-registered SLCs, and , the phase of the interferogram is given by:
which is only known modulo . Thus, a phase unwrapping algorithm is applied to determine the unwrapped phase, .
Moving forward we assume these quantities have been corrected for topography and relative shifts so the result is due only to motion.
Raw Measurements

## Slide 9
Vector Ice Velocity Measurements
    Ignores submergence/emergence velocity (upward or downward motion to accommodate snowfall/melt).
Ideally vector measurements require data from three track-directions.
With a surface-parallel flow assumption, the velocity vector is determined using only two directions by assuming it lies in plane tangent to the surface.

## Slide 10
Velocity with Offsets and the Surface Parallel Assumption
The line of sight displacement is:
Solving for horizontal displacement:
Assuming surface parallel flow:
Combining yields:
Velocity in radar-directed coordinates is and .

## Slide 11
The rotation angle of the radar cross-track coordinates with respect to North is:
The angle relative to north for a point is:
.
Horizontal velocities are then:
.
Radar to Polar Stereographic Coordinates

## Slide 12
,
,
.
For crossing orbits and unwrapped phases, velocity is given by:
Crossing Orbit Solution

## Slide 13
Range-azimuth offsets from a single orbit track,
Unwrapped phase (for range) with azimuth offsets from a single orbit track,
Range-range offsets from crossing orbit tracks, and
Unwrapped phase-phase data from crossing orbits.
Possible Combinations
In practice the final result is often the inverse error weighted combination of the available data to provide the optimal result.

## Slide 14
It may be desirable to include additional weights (e.g, feathering). In this case the weights are given by:
.
Multiple data are combined to produce an estimate:
=.
The uncertainty for the weighted estimate is:
Final Weighted Solution

## Slide 15
Tidal motion and grounding line detection
For pair 1-2 interferogram:
For pair 2-3 interferogram:
For ~ difference is: )/
Grounding line at inner limit of tidal fringes: ~ 0
Rignot, Ann. Glaciol. 1998

## Slide 16
Implementation
Algorithms just described are fairly generic but there are multiple ways to implement.

## Slide 17
NASA Supported L3/L4 Processors
There are several other systems supported by ESA and other space agencies.

## Slide 18
GrIMP Implementation
Rosen, Project Scientist
This document contains export-restricted data.
Speckle Tracking
Interferograms
Ionosphere Correction
Mosaicking
Calibration
LSQFit
Calibration
LSQFit
L1 – SAR SLCs
L2 – Offsets/Interferograms
L3 – Gridded Mosaics
Input is 100s to 1000s of SLCs for continental scale mosaic.
In current processing calibration step LSQ fit for unknown constants (with S1 orbits single constant for each pair).
Mosaicking computes an error-weighted average of all estimates (phase/offsets).

## Slide 19
Pseudo Validation
Comparison of annual map with GPS points collected along the nominal 2000-m contour by NASA in the 1990s.
Not a true validation since its unclear what the relative contributions of errors and true change are to the differences.

## Slide 20
MEaSUREs-3 Antarctica Implementation
Rosen, Project Scientist
This document contains export-restricted data.
Speckle Tracking
Phase only
Ionosphere Correction
Calibration
Mosaicking
Calibration
Mosaicking
L1 – SAR SLCs
L2 – Offsets/Interferograms
L3 – Gridded Mosaics
Input is 1000s of SLCs (S1, RADARSAT-2, Envisat ASAR, ALOS PALSAR, CSK-2G) for continental scale mosaic.
Automatic calibration with slow moving areas from reference velocity map.
Both speckle tracking (annual to monthly) and phase only (multi-annual) include error estimates.
Phase map assumes surface parallel flow. Prototype 3D phase map uses multiple tracks.
L4 product -BedMachine
Speckle tracking
Phase only

## Slide 21
Deep learning
MEaSUREs-3 Antarctica Implementation
Rosen, Project Scientist
This document contains export-restricted data.
Interferograms
Differential
L1 – SAR SLCs
L2 – Offsets/Interferograms
Input is 1000s of SLCs (S1, CSK-2G) for continental scale mosaic.
Machine learning algorithm to pick grounding lines.
Time series of grounding lines used to define grounding zones (yearly to monthly).

## Slide 22
ITS_LIVE MeASUREs
High Mountain Asia
Canadian Arctic
Alaska
Russia and Svalbard

## Slide 23
Cal/Val Approach:
Science Team generates L3 products.
Products are validated against GNSS and other data in Jupyter notebooks.
Cryosphere Cal/Val
The project will support 16 GNSS ice sheet stations (other contributions welcome).

## Slide 24
Overall Cal/Val Process
GNSS Sites
UNAVCO
Iridium
NISAR Cal/Val Database
L0/L2 Processor
ST L3 Algorithms
Jupyter Notebooks
Validation Report for given period and requirement
L3 products & cal/val data
L3 products
GNSS data

## Slide 25
ATBD documents, Notebooks, and supporting code are all available through project gitlab site: https://gitlab.com/nisar-science-algorithms/cryosphere/nisarcryocalvalnotebooks
Which mirrors: https://github.com/fastice/nisarCryoCalValNotebooks
The notebooks can all be demonstrated using “launch binder” button.
Proof of concept is with GrIMP products at NSIDC but will be modified to pull full range of products on NISAR cal/val server.

## Slide 26
Validation Notebooks - Introduction

## Slide 27
Validation Notebooks - Overview

## Slide 28
Validation Notebooks - Results

## Slide 29
Cryosphere ATBD
Questions?